Product Data Sheet

Product Description & Main Application

Samic Nova Ferrous CF-4 series are diesel engine oils formulated with high quality base stocks and selected additives to ensure optimum performance and protection for diesel engines requiring an API CF-4 specification. Suitable for diesel engines for both turbocharged and normally aspirated engines operating under severe service conditions in all seasons.

Performance & Customer Benefits

- Good oxidation & thermal stability reduces sludge build up and keeps the engine cleaner.

- Optimum wears protection to extend engine efficiency and service life.

- Improved fuel economy, due to high fluidity at low temperatures.

- Reduced oil consumption at high operating engine temperatures.

- Improved resistance to deposit formation keeps engine clean to give your vehicle maximum power under extreme operating conditions.

- Optimum TBN reserves provide improved acid neutralization and corrosion protection, especially in old heavy duty diesel engines.

Specifications & Recommendations

Samic Nova Ferrous meets or exceeds following International and Builder specifications:

- API  CF-4, CF, SJ

- ACEA E2

- MTU OIL Category-1

- MAN 270/271

- VOLVO VDS

- Deutz DQC –I-05

- MB 228.0/1

Typical Physical Characteristics

| Samic Nova Ferrous | Test Method | Units | 20W-40 | 20W-50 |
| --- | --- | --- | --- | --- |
| Density @ 15 0C | ASTM D 4052 | gm/cc | 0.888 | 0.890 |
| Viscosity @ 100 0C | ASTM D 445 | cSt | 14.30 | 21.4 |
| Viscosity @ 40 0C | ASTM D 445 | cSt | 107 | 182 |
| Viscosity Index | ASTM D 2270 | - | 137 | 137 |
| Pour Point | ASTM D 97 | °C | -30 | -30 |
| Flash Point (COC) | ASTM D 92 | °C | 230 | 236 |
| Total Base Number | ASTM D 2896 | mg KOH/g | 8.0 | 8.0 |
| CCS Viscosity | ASTM D 5293 | cP | 6020 @ -15 °C | 6020 @ -15 °C |

The above figures are typical of blends with normal production tolerance and do not constitute a specification.

For further information, please contact: sales@samiclubricants.com

# Text boxes

Samic Nova Ferrous CF-4 series

High Performance Multigrade Diesel Engine Oil